Rendering strategy of passThruAttributes.

Description:
This document is design to manifest the problem with existing strategy of rendering of passThru attributes and the solution.

Note: There are 68 possible passThru attributes according to the existing passThruAttributes class which includes effect related attributes as well.

As we can see in above diagrams that there are two types of attributes with different nature depending on their assigned value. To render passThru attributes above factors need to be considered.

Issues with existing strategy.

1- In the RenderResponse phase each component iterate through the list of 68 passThruAttributes to render passThruAttributes on root element of the component even if there wasn't any pass thru attribute set on the component. (inefficient)

2- Couple of renderers checks if there was any passThruAttribute set on the component using the (uiComponent.getAttributes().size()>1) before iterating on passThruList, but this method gives wrong information in most of the cases. (invalid)

(e.g.) if a page have 20 to 30 components on, then the iteration would be reach to1360 to 2040 cycles.

Why the map.size() could be invalid?

The JSF's implementation of AttributeMap puts only those attributes in the map where setter/getter are not defined in the component class for that attribute and if the value of the attribute is not binded with the bean. So that is the why keyset of the map do not provide proper information unless each attribute get examined one by one using the MAP.get(key) method.

Solution:
To deal with these issues, we have created our own implementation of AttributeMap, which wraps the real map and keep track of all boolean and non-boolean passThru attributes on the component. That allows Icefaces to iterate through only those attributes that are defined on the component. So if there isn't any passThru attribute set on the component, then no iteration requires and if two attributes are set on the component then two cycles of iteration will happen.

Backwards compatibility:
To keep existing approach intact that let standard components to use old strategy, we have introduced an interface called com.icesoft.faces.component.IcePassThruAttribute. That tells icefaces to use difference mechanisam to render passThruAttributes for particulare component.

Renderer does not require any changes, same call needs to be make as before to renderPassThru attributes.
        PassThruAttributeRenderer
        .renderAttributes(facesContext, uiComponent, null);

passthru attributes can also be excluded, as before.
        HashSet excludes = new HashSet();
        excludes.add("style");

        PassThruAttributeRenderer.
        renderAttributes(
        facesContext, uiComponent, getExcludesArray(excludes));

How to use new strategy:
The component need to implement the IcePassThruAttribute interface and override the following two methods in the component class.

Note: Due to the hierarchy restriction we are not able to overide the following methods in any of the base class. So we have to override them in each of the component class separately. These methods do not require any modification, methods can be copy and pasted as it is.

 public Map getAttributes() {
Map attMap = super.getAttributes();
   if (!attMap.containsKey(IcePassThruAttributes.ICE_ATTRIBUTE_MAP)) {
        Map newMap = new AttributesMap(attMap);
        attMap.put(IcePassThruAttributes.ICE_ATTRIBUTE_MAP,newMap);
        return newMap;
        } else {
        return (Map)attMap.get(IcePassThruAttributes.ICE_ATTRIBUTE_MAP);
        }
 }

public void setValueBinding(String name, ValueBinding vb) {
        Map iceAttributeMap =
(Map)getAttributes().get(IcePassThruAttributes.ICE_ATTRIBUTE_MAP);
        if (name != null && iceAttributeMap != null) {
        if (PassThruAttributeRenderer.passThruAttributeNames.contains(name)) {
((List)iceAttributeMap.
      get(IcePassThruAttributes.PASS_THRU_NON_BOOLEAN_ATT_LIST)).
add(name);
        } else if (PassThruAttributeRenderer.
booleanPassThruAttributeNames.contains(name)) {
((List)iceAttributeMap.
get(IcePassThruAttributes.PASS_THRU_BOOLEAN_ATT_LIST)).add(name);
        }
        }
        //you can put your code here if any
        super.setValueBinding(name, vb);
}
--------
NOTE: We have tested the execution time before and after the changes. The component execution time was twice as fast and the page execution time was 10% to 15% fast with new changes.

-- Adnan Durrani --